## Slide 1
IBM3118 | AC4 | SBrT 2026
Beehive Monitoring
Six references that shape a low-cost, non-invasive monitoring system
ENVIRONMENT
ENTRANCE
ACOUSTICS + IoT
Igor Costa · Jorge Alves · Ian Dias · Davi Ito
01

## Slide 2
AC4 | CONTEXT
One signal is not enough to monitor a hive
02
The literature supports a multimodal view of the colony.
01 CONTEXT
Manual inspections are intermittent and may disturb the colony when the hive is opened repeatedly.
02 DATA PIPELINE
IoT systems connect environmental sensors, audio/video capture, wireless communication and remote storage.
03 RESEARCH GAP
Signals are promising, but thresholds, metrics and cross-colony validation are not standardized.
Project direction: combine DHT11 measurements, entrance imaging and wireless data collection; treat audio, vibration and event detection as validation-dependent extensions.
Fontes: [1]--[6], as listed in references.bib
2

## Slide 3
REF. 1 | LITERATURA
Zheng et al. connect hive conditions to activity
03
APPROACH
Temperature and humidity at center, margin, entrance and outside.
Internal sound sensor plus entrance-facing webcam.
YOLOv5 + DeepSORT for multi-bee tracking.
QUALITATIVE TAKEAWAY
A strong example of multimodal IoT monitoring: environmental measurements are interpreted together with entrance activity and internal sound.
QUANTITATIVE EVIDENCE
83.5 ± 0.7
MOTA
77.3 ± 0.2
MOTP
16 fps
maximum reported rate
25–37 °C
center temperature range
PROJECT IMPLICATION
Supports the sensor distribution, entrance camera and multimodal architecture. The reported environmental ranges are evidence from one study, not universal thresholds.
Fontes: Zheng et al. (2024), Smart Agricultural Technology, DOI 10.1016/j.atech.2024.100584
3

## Slide 4
REF. 2 | LITERATURA
IntelliBeeHive: low-cost vision with clear limits
04
APPROACH
Entrance-facing camera and account-based remote monitoring.
YOLOv7-tiny models for bees, pollen and mites.
Designed for low-cost, real-time observation.
QUALITATIVE TAKEAWAY
The paper demonstrates that lightweight computer vision can monitor the hive entrance without disturbing the colony, but the Varroa result must remain a proof of concept.
QUANTITATIVE EVIDENCE
96.28%
tracking accuracy
0.8319
pollen F1-score
YOLOv7
tiny variant
Limited
mite data
PROJECT IMPLICATION
Supports the ESP32-CAM / lightweight-model direction. Pollen and Varroa require representative labeled data before being treated as reliable outputs.
Fontes: Narcia-Macias et al. (2024), ICMLA, DOI 10.1109/ICMLA61862.2024.00122; open preprint: arXiv:2309.08955
4

## Slide 5
REF. 3 | LITERATURA
Acoustic sensing lacks standard metrics
05
APPROACH
Review of microphones and accelerometers for beekeeping.
Focus on queen presence and swarming-related states.
Signals can be collected without opening the hive.
QUALITATIVE TAKEAWAY
The review supports acoustic and vibration monitoring as a complementary, non-invasive modality, while emphasizing that results are difficult to compare across colonies and studies.
QUANTITATIVE EVIDENCE
N/A
pooled score
Small
datasets
No
common metrics
Low
generalizability
PROJECT IMPLICATION
The project should preserve signal context and document feature extraction. The KY-038 can only be an initial noise indicator; reliable recording needs a suitable microphone.
Fontes: Uthoff et al. (2023), Computers and Electronics in Agriculture, DOI 10.1016/j.compag.2022.107589
5

## Slide 6
REF. 4 | LITERATURA
Beemon builds a remote monitoring pipeline
06
APPROACH
Temperature, humidity, weight, audio and video capture.
MQTT to ThingsBoard and remote server storage.
Continuous operation in an outdoor apiary.
QUALITATIVE TAKEAWAY
Beemon focuses on reliable data acquisition and remote access. Its contribution is the end-to-end monitoring infrastructure rather than a fully validated colony-health classifier.
QUANTITATIVE EVIDENCE
44.1 kHz+
audio capability
Near-real
time collection
Outdoor
continuous operation
Limited
field results
PROJECT IMPLICATION
Supports MQTT, timestamped records, remote visualization and a separation between embedded capture and heavier analysis on a server.
Fontes: Tashakkori, Hamza & Crawford (2021), Computers and Electronics in Agriculture, DOI 10.1016/j.compag.2021.106427
6

## Slide 7
REF. 5 | LITERATURA
Wireless sensing can monitor hive conditions
07
APPROACH
Wireless network for in-hive temperature, relative humidity and sound.
Wi-Fi evaluated in an apiary environment.
Signals interpreted in relation to stress and swarming.
QUALITATIVE TAKEAWAY
The study provides evidence that wireless collection is practical, while also warning that radio-frequency effects and hive dynamics require continued evaluation.
QUANTITATIVE EVIDENCE
6 hives
study scale
30 days
observation period
No change
Wi-Fi effect
Real-time
monitoring potential
PROJECT IMPLICATION
Supports Wi-Fi as the first communication option when coverage exists. The final deployment still needs testing for range, power and environmental stability.
Fontes: Henry et al. (2019), Computers and Electronics in Agriculture, DOI 10.1016/j.compag.2018.11.001
7

## Slide 8
REF. 6 | LITERATURA
Raspberry Pi enables entrance monitoring
08
APPROACH
Low-cost Raspberry Pi video system at the hive entrance.
Background subtraction for segmentation.
Counts bees, identifies position and measures in/out activity.
QUALITATIVE TAKEAWAY
Tu et al. show that entrance behavior can be estimated with a lightweight embedded platform, using manual counts as the reference for evaluation.
QUANTITATIVE EVIDENCE
0.987
R²: bee count
0.953
R²: in-activity
0.888
R²: out-activity
Real-time
processing viable
PROJECT IMPLICATION
Supports low-cost entrance imaging and objective validation. The method must be retested under our camera position, lighting and entrance geometry.
Fontes: Tu et al. (2016), Computers and Electronics in Agriculture, DOI 10.1016/j.compag.2016.01.011
8

## Slide 9
SYNTHESIS
Six studies point to one practical architecture
09
WHAT THE LITERATURE SUPPORTS
Environmental sensing inside and outside the hive.
Entrance-focused vision with lightweight processing.
Wireless transport, remote storage and visualization.
WHAT REMAINS OPEN
No universal thresholds for colony state.
Acoustic metrics and datasets are inconsistent.
Varroa and event detection need field validation.
OUR INITIAL SCOPE
DHT11 + ESP32-CAM + wireless controller.
Timestamped environmental and image data.
Audio/vibration as experimental extensions.
Takeaway: the contribution is not a single sensor or model; it is a validated multimodal data pipeline for non-invasive hive monitoring.
Fontes: [1]--[6], as listed in references.bib
9

## Slide 10
SOURCES
References used in the AC4 presentation
10
[1] Zheng et al. (2024). Intelligent beehive monitoring system based on IoT and colony state analysis. DOI: 10.1016/j.atech.2024.100584
[2] Narcia-Macias et al. (2024). IntelliBeeHive: automated honey bee, pollen and Varroa monitoring. DOI: 10.1109/ICMLA61862.2024.00122
[3] Uthoff et al. (2023). Acoustic and vibration monitoring of honeybee colonies. DOI: 10.1016/j.compag.2022.107589
[4] Tashakkori, Hamza & Crawford (2021). Beemon: an IoT-based beehive monitoring system. DOI: 10.1016/j.compag.2021.106427
[5] Henry et al. (2019). Precision apiculture: wireless sensor network for honeybee hives. DOI: 10.1016/j.compag.2018.11.001
[6] Tu et al. (2016). Automatic behaviour analysis system for honeybees using computer vision. DOI: 10.1016/j.compag.2016.01.011
Use the article's references.bib for the complete BibTeX records.
Fontes: Publisher records, DOI pages and the open arXiv preprint listed above
10